## Slide 1: AXI Stream Design

## Slide 2: Master AXI-Stream Specification
Send user provided data by AXI-Stream Protocol
  User provides needed data to send to data input
  When user activates send, the module should send user provided data by AXI-Stream. Send is async signal.
  After finish sending should activate finish output for 1 cycle
Master AXI-Stream
data[31:0]
send
finish
tvalid
tready
tlast
tdata[31:0]
aclk
areset_n

## Slide 3: Slave AXI-Stream Specification
Receives AXI-Stream Master Provided Data
  AXI-Stream Master sends data through AXI-Stream
  When user application is ready to accept, enables ready input – can be only pulse signal
  AXIS Slave Receives that data and puts on data output
  Enables finish signal after receiving the data, to notify user
Slave AXI-Stream
data[31:0]
ready
finish
tvalid
tready
tlast
tdata[31:0]
aclk
areset_n

## Slide 4: Simulate AXI-Stream System
We will connect our designed AXI-Stream Master and Slave
Exchange the data between them
Master AXI-Stream
data[31:0]
send
finish
tvalid
tready
tlast
tdata[31:0]
aclk
areset_n
Slave AXI-Stream
data[31:0]
ready
finish
tvalid
tready
tlast
tdata[31:0]
aclk
areset_n
TB